## Slide 1: Microprocessors and Microcontrollers
Basic Connection

## Slide 2: Needed Equipments
Microcontroller – ATmega32
The AVR Programmer / Loader
  To load your code into the mc

## Slide 3: Steps
Connect USBasp to PC
(Windows) Check Driver from Device Manager. If problem, update driver using zadig.
Install Extreme Burner
Connect USBasp with ATmega32
Write Code in Atmel
Upload hex to Atmega32 using Extreme Burner

## Slide 4: USBasp Programmer

## Slide 5: USBasp Programmer Driver Troubleshoot (only for Windows 10)
(Step 1: Installing the USBasp Driver Using Zadig) https://www.instructables.com/Programming-Microcontrollers-With-a-USBasp-Program/

## Slide 6
USBasp Programmer Driver Troubleshoot (only for Windows 10)

## Slide 7: USBasp Programmer Driver Troubleshoot (only for Windows 10)
(Step 1: Installing the USBasp Driver Using Zadig) https://www.instructables.com/Programming-Microcontrollers-With-a-USBasp-Program/

## Slide 8: Burner
Extreme Burner
  http://extreme-burner-avr.software.informer.com/download/
There is also avrpal, avrdude
Loads the HEX file into microcontroller

## Slide 9: Burner

## Slide 10: Needed Softwares
AVR Studio
  https://www.microchip.com/mplab/avr-support/atmel-studio-7
  Atmel Studio 7.0 (build 1931) offline installer
This is the IDE

## Slide 11: Writing Code
Create New Project
Select “GCC C Executable Project”
Select path to save the project
  You will later need this path for the hex file
Then select device type
  Search for ATmega 32
Now you can write the program

## Slide 12: Compile the hex code
Finish the program
Select “Build Solution (F7)” from the Build Menu
You will find that a hex file is generated in the Debug folder
The name of the hex file will be the same as your project name

## Slide 13: Connecting ATmega32 with programmer
Following the figure connect the 6 corresponding microcontroller pins with the loader.
Be careful about the orientation of the cable layout. The extended part goes to the right

## Slide 14: Connecting ATmega32 with programmer
1 = VCC (5V)
2 = MOSI
3 = GND
6 = RST
8 = SCK
10 = MISO
Depending on the connection of USBasp programmer, you may have to swap odd pins with even ones (e.g. 1 <-> 2, 3 <-> 4, 5 <-> 6 and so on)

## Slide 15
1 = VCC
2 = MOSI
3 = GND
6 = RST
8 = SCK
10 = MISO

## Slide 16: Connecting ATmega32 with programmer
Follow the red wire/stripped wire.
This wire should be #1 pin (VCC).

## Slide 17: Today’s Task

## Slide 18: Today’s Task

## Slide 19: Today’s Task

## Slide 20: Today’s Task

## Slide 21: Connecting ATmega32 with programmer (Without Cable)
https://www.youtube.com/watch?v=bH8c8sMLfCI
Courtesy: Shanjinur Islam Spondon, CSE 15

## Slide 22: Placing ATmega32 on Breadboard
https://www.youtube.com/watch?v=bH8c8sMLfCI
Courtesy: Shanjinur Islam Spondon, CSE 15

## Slide 23: Breadboard

## Slide 24: Breadboard

## Slide 25: Load the hex into mc
Run Extreme Burner
Load the hex file into it by “Open” and locate your hex file
From menu select Chip -> ATmega32
Set the microcontroller on the AVR Programmer
Connect the programmer with PC
In extreme Burner select the menu “write” and choose “Flash”

## Slide 26: Load the hex into mc

## Slide 27: Setting mc in the AVR Programmer (USBasp alternative)
For the big loaders from TechshopBD
  The upper portion (U) side goes closer to the side with the liver
  There is a push button
  Push it so that the yellow LED is on and the red one is off

## Slide 28: Complete Process of Programming a Microcontroller
Write the code
  In ATMEL Studio, or other IDE
Compile it to a .hex file.
  For ATMEL Studio, you will find the hex on the “Debug” folder in your project

## Slide 29: Complete Process of Programming a Microcontroller
3. Inserting the .hex file into the microcontroller
  Load the hex file into burner
  set the microcontroller on the “AVR Programmer”
  Write
4. Set the microcontroller in the working circuit

## Slide 30
☺